## Slide 1: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching

## Slide 2: The MAC Sublayer
Responsible for deciding who sends next on a multi-access link
  An important part of the link layer, especially for LANs
Physical
Link
Network
Transport
Application
MAC is in here!

## Slide 3: Multiple Access Problem
An example: a classroom
Human protocols:
  “Give everyone a chance to speak”
  “Don’t speak until you are spoken to”
  “Don’t monopolize the conversation”
  “Raise your hand if you have a question”
  “Don’t interrupt when someone is speaking”
  “Don’t fall asleep when someone else is talking”
  In LANs, WiFi, satellite networks, cocktail party
  If more than 2 users send at the same time - collision
  All collided packets are lost -> waste of bandwidth

## Slide 4: Channel Allocation Problem (1)
For fixed channel and traffic from N users
  Divide up bandwidth using FDM, TDM, CDMA, etc.
  This is a static allocation, e.g., FM radio
This static allocation performs poorly for bursty traffic
  Allocation to a user will sometimes go unused
  Dynamic allocation gives the channel to a user when they need it.
  Potentially N times as efficient for N users.

## Slide 5: Channel Allocation Problem (2)
Schemes vary with assumptions:
Assumption | Implication
Independent traffic | Often not a good model, but permits analysis
Single channel | No external way to coordinate senders
Observable collisions | Needed for reliability; mechanisms vary
Continuous or slotted time | Slotting may improve performance
Carrier sense | Can improve performance if available
Notes: In random-access or contention no station is superior to another station and
none is assigned control over another.
At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send. This decision depends on the state of the medium (idle or busy).

## Slide 6: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching

## Slide 7: Multiple Access Protocols
  ALOHA »
  CSMA (Carrier Sense Multiple Access) »
  Collision-free protocols »
  Limited-contention protocols »
  Wireless LAN protocols »

## Slide 8: ALOHA Network
Developed by Norm Abramson at the Univ. of Hawaii
  the guy had interest in surfing and packet switching
  mountainous islands → land-based network difficult to install
  fully decentralized protocol
ACK
ACK
ACK
ACK
Notes: ALOHA(Additive Link On-Line Hawaii system)

## Slide 9: Pure ALOHA
In pure ALOHA, users transmit frames whenever they have data; users retry after a random time for collisions
  Efficient and low-delay under low load
`
Collision
Collision
Time
User
A
B
C
D
E
Notes: ALOHA, the earliest random access method, was developed at the University of Hawaii in early 1970.
It was designed for a radio (wireless) LAN, but it can be used on any shared medium.
It is obvious that there are potential collisions in this arrangement. The medium is shared between the stations. When a station sends data, another station may attempt to do so at the same time. The data from the two stations collide and become garbled.

## Slide 10: Vulnerable Period
Collisions happen when other users transmit during a vulnerable period that is twice the frame time
  Synchronizing senders to slots can reduce collisions
Frame time: the frame length divided by the bit rate

## Slide 11: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps.
What is the requirement to make this frame collision-free?
Solution
Frame time is 200 bits/200 kbps or 1 ms.
The vulnerable time is 2 × 1 ms = 2 ms.
This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the period (1ms) that this station is sending.

## Slide 12: Channel Utilization (1)
An infinite collection of users; Fixed-length frame
New frames generated by the stations are modeled by a Poisson distribution with a mean of frames per frame time.
  For reasonable throughput,
The old (retransmitted) and new frames combined are modeled by a Poisson distribution with a mean of frames per frame time.
Throughput per frame time S = GP0,
  P0 is the probability of a transmission succeeding ---- a frame does not suffer a collision.

## Slide 13: Channel Utilization (2)
The probability that frames are generated during a frame time, in which frames are expected, is given by the Poisson distribution
The mean number of frames generated in the vulnerable period (an interval two frame times long):
The probability of no frames being initiated during the entire vulnerable period:
Throughput:
  maximum at with

## Slide 14: Slotted ALOHA
Slotted ALOHA is twice as efficient as pure ALOHA
  Low load wastes slots, high loads causes collisions
  Efficiency up to 1/e (37%) for random traffic models
  Applied in Internet access over cable, multiple RFID tags talk to the same RFID reader

## Slide 15: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps.
What is the throughput if the system (all stations together) produces
a. 1000 frames per second?
b. 500 frames per second?
c. 250 frames per second?

## Slide 16: Solution
The frame time is 200 bits/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, or 1 frame per millisecond, then G = 1. In this case S = G × e−2G = 0.135 (13.5%). This means that the throughput is 1000 × 0.135 = 135 frames. Only 135 frames out of 1000 will probably survive.
b. If the system creates 500 frames per second, or 1/2 frames per millisecond, then G = 1/2. In this case S = G × e−2G = 0.184 (18.4%). This means that the throughput is 500 × 0.184 = 92. Only 92 frames out of 500 will probably survive.
c. If the system creates 250 frames per second, or 1/4 frames per millisecond, then G = 1/4. In this case S = G× e−2G = 0.152 (15.2%). This means that the throughput is 250 × 0.152 = 38. Only 38 frames out of 250 will probably survive

## Slide 17: Multiple Access Protocols
  ALOHA »
  CSMA (Carrier Sense Multiple Access) »
  Collision-free protocols »
  Limited-contention protocols »
  Wireless LAN protocols »

## Slide 18: CSMA (1)
CSMA improves on ALOHA by sensing the channel!
  User doesn’t send if it senses someone else
  Based on the principle “sense before transmit” or “listen before talk.”
Notes: 802.11 uses a refinement of p-persistent CSMA

## Slide 19: Behavior of three persistence methods
Variations on what to do if the channel is busy:
  1-persistent (greedy) sends as soon as idle
  Nonpersistent waits a random time then tries again
  p-persistent sends with probability p when idle

## Slide 20: Flow diagram for three persistence methods

## Slide 21: Performance of CSMA
CSMA outperforms ALOHA, and being less persistent is better under high load

## Slide 22: CSMA with Collision Detection
CSMA/CD improvement is to detect/abort collisions
  Reduced contention times improve performance
  A station monitors the medium after it sends a frame to see if the transmission was successful.
    If so, the station is finished.
    If there is a collision, the frame is sent again.
Collision time is much shorter than frame time

## Slide 23: Collision of the first bit in CSMA/CD

## Slide 24: Collision and abortion in CSMA/CD

## Slide 25: Flow diagram for CSMA/CD

## Slide 26: Example
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal) is 25.6 μs, what is the minimum size of the frame?
Solution
The minimum frame transmission time is 2 × Tp = 51.2 μs. This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision.
The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet, as we will see later in the chapter.

## Slide 27: Multiple Access Protocols
  ALOHA »
  CSMA (Carrier Sense Multiple Access) »
  Collision-free protocols »
  Limited-contention protocols »
  Wireless LAN protocols »

## Slide 28: Collision-Free (1) – Bitmap
Collision-free protocols avoid collisions entirely
  Senders must know when it is their turn to send
The basic bit-map protocol:
  Sender set a bit in contention slot if they have data
  Senders send in turn; everyone knows who has data
Notes: reservation: a station needs to make a reservation before sending data. Time is divided into intervals. In each interval, a reservation frame precedes the data frames sent in that interval.

## Slide 29: Collision-Free (2) – Token Ring
Token sent round ring defines the sending order
  Station with token may send a frame before passing
  Idea can be used without ring too, e.g., token bus
Station
Direction of
transmission
Token
Notes: Token ring: the stations in a network are organized in a logical ring. For each station, there is a predecessor and a successor. The predecessor is the station which is logically before the station in the ring; the successor is the station which is after the station in the ring.

## Slide 30: Collision-Free (3) – Countdown
Binary countdown improves on the bitmap protocol
  Stations send their address in contention slot (log N bits instead of N bits)
  Medium ORs bits; stations give up when they send a “0” but see a “1”
  Station that sees its full address is next to send

## Slide 31: Multiple Access Protocols
  ALOHA »
  CSMA (Carrier Sense Multiple Access) »
  Collision-free protocols »
  Limited-contention protocols »
  Wireless LAN protocols »

## Slide 32: Limited-Contention Protocols (1)
Idea is to divide stations into groups within which only a very small number are likely to want to send
  Avoids wastage due to idle periods and collisions
Already too many contenders for a good chance of one winner

## Slide 33: Limited Contention (2) –Adaptive Tree Walk
Tree divides stations into groups (nodes) to poll
  Depth first search under nodes with poll collisions
  Start search at lower levels if >1 station expected
Level 0
Level 1
Level 2
At what level in the tree should the search begin?
Each node at level I has a fraction 2-i of the stations below it.
If the number of ready stations is q and uniformly distributed, the mean number of contending stations per slot is 1. i.e., 2-i q = 1
i =log2q

## Slide 34: Multiple Access Protocols
  ALOHA »
  CSMA (Carrier Sense Multiple Access) »
  Collision-free protocols »
  Limited-contention protocols »
  Wireless LAN protocols »

## Slide 35: Wireless LAN Protocols
Wireless has complications compared to wired.
Nodes may have different coverage regions
  Leads to hidden and exposed terminals
Nodes can’t detect collisions, i.e., sense while sending
  Makes collisions expensive and to be avoided

## Slide 36: Hidden terminals
Hidden terminals are senders that cannot sense each other but nonetheless collide at intended receiver
  Want to prevent; loss of efficiency
  A and C are hidden terminals when sending to B

## Slide 37: Exposed terminals
Exposed terminals are senders who can sense each other but still transmit safely (to different receivers)
  Desirably concurrency; improves performance
  B  A and C  D are exposed terminals

## Slide 38: Multiple Access with Collision Avoidance
MACA protocol grants access for A to send to B:
  A sends RTS to B [left]; B replies with CTS [right]
  A can send with exposed but no hidden terminals
  A sends RTS to B; C and E hear and defer for CTS
  B replies with CTS; D and E hear and defer for data
Notes: This protocol solves the issue of expensive collisions too, since the RTS/CTS are short packets – if there is a collision it will be brief, not as long as a data frame.

## Slide 39: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching

## Slide 40: Ethernet
  Classic Ethernet »
  Switched/Fast Ethernet »
  Gigabit/10 Gigabit Ethernet »
802.3
802.3u
802.3z
802.3ae

## Slide 41: Ethernet
“Dominant” LAN technology developed in the 1970s by Robert Metcalfe and David Boggs.
  First widely used LAN technology
  Simpler, cheaper than token LANs and ATM
  Kept up with speed race: 10, 100, 1000 Mbps 10Gbps, …
Metcalfe’s Ethernet
sketch

## Slide 42: Classic Ethernet – Physical Layer
One shared coaxial cable to which all hosts attached
  Up to 10 Mbps, with Manchester encoding
  Hosts ran the classic Ethernet protocol for access

## Slide 43: Classic Ethernet – Implementation

## Slide 44: Classic Ethernet – 10Base5 and 10Base2

## Slide 45: Classic Ethernet – 10BaseT and 10BaseF

## Slide 46: Classic Ethernet – MAC and Frame
MAC protocol is 1-persistent CSMA/CD (earlier)
  Random delay (backoff) after collision is computed with BEB (Binary Exponential Backoff)
  Frame format is still used with modern Ethernet.
Ethernet
(DIX)
IEEE 802.3

## Slide 47: Classic Ethernet – CSMA/CD
Collisions can occur and take as long as 2 to detect
   is the time it takes to propagate over the Ethernet
  Leads to minimum packet size for reliable detection

## Slide 48: Classic Ethernet – CSMA/CD with BEB

## Slide 49: Classic Ethernet – Addressing
Each station on an Ethernet network (such as a PC, workstation, or printer) has its own network interface card (NIC).
The NIC fits inside the station and provides the station with a link-layer address.
The Ethernet address is 6 bytes (48 bits), normally written in hexadecimal notation, with a colon between the bytes.
For example, the following shows an Ethernet MAC address:
4A:30:10:21:10:1A
You can use “ipconfig /all” to check the MAC addresses of your PC or laptop.

## Slide 50: Classic Ethernet – unicast and multicast address
To find the type of the address, we need to look at the second hexadecimal digit from the left.
  If it is even, the address is unicast.
  If it is odd, the address is multicast.
  If all digits are Fs, the address is broadcast.

## Slide 51: Example
Define the type of the following destination addresses:
4A:30:10:21:10:1A
47:20:1B:2E:08:EE
FF:FF:FF:FF:FF:FF
Solution
  a. This is a unicast address because A in binary is 1010 (even).
  b. This is a multicast address because 7 in binary is 0111 (odd).
  c. This is a broadcast address because all digits are Fs in
  hexadecimal.

## Slide 52: Classic Ethernet – Performance
Efficient for large frames, even with many senders
  Degrades for small frames (and long LANs)
10 Mbps Ethernet,
64 byte min. frame

## Slide 53: Classic Ethernet – Bandwidth sharing

## Slide 54: Collision domains
A bridge is the separation of the collision domain

## Slide 55: Full-duplex Switched Ethernet

## Slide 56: Switched/Fast Ethernet (1)
  Hubs wire all lines into a single CSMA/CD domain
  Switches isolate each port to a separate domain
    Much greater throughput for multiple ports
    No need for CSMA/CD with full-duplex lines

## Slide 57: Switched/Fast Ethernet (2)
Switches can be wired to computers, hubs and switches
  Hubs concentrate traffic from computers
  More on how to switch frames the in 4.8
Switch
Twisted pair
Switch ports
Hub

## Slide 58: Switched/Fast Ethernet (3)
Fast Ethernet extended Ethernet from 10 to 100 Mbps
  The MAC sublayer was left unchanged.
  To keep the minimum size of the frame, the maximum length of the network should be 10 times shorter
  Twisted pair (with Cat 5) dominated the market

## Slide 59: Encoding for fast Ethernet

## Slide 60: Gigabit / 10 Gigabit Ethernet
Switched Gigabit Ethernet is now the garden variety
  With full-duplex lines between computers/switches

## Slide 61: Gigabit / 10 Gigabit Ethernet – operation mode
The address length, the frame format, and the maximum and minimum frame length are kept the same.
To achieve a data rate of 1 Gbps, this was no longer possible to keep the MAC sublayer untouched.
Gigabit Ethernet has two distinctive approaches for medium access:
  half-duplex: used with a hub. CSMA/CD required. The maximum distance is 100 times less than that in classic Ethernet (2500m25m).
  full-duplex: “normal” mode. Used in central switch. buffered. No contention, no CSMA/CD

## Slide 62: Gigabit / 10 Gigabit Ethernet – network radius
Two features to the standard to increase the radius:
Carrier extension: tells the hardware to add its own padding after the normal frame(64 bytes) to extend the frame to 512 bytes.
Frame bursting: allows a sender to transmit a concatenated sequence of multiple frames in a single transmission.
These two features extend the radius of the network to 200 meters.

## Slide 63: Gigabit / 10 Gigabit Ethernet – implementation
  Gigabit Ethernet is commonly run over twisted pair
  10 Gigabit Ethernet is being deployed where needed
  40/100 Gigabit Ethernet is under development

## Slide 64: Encoding in Gigabit Ethernet

## Slide 65: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching

## Slide 66: Wireless LANs
  802.11 architecture/protocol stack »
  802.11 physical layer »
  802.11 MAC »
  802.11 frames »

## Slide 67: 802.11 Architecture/Protocol Stack (1)
Wireless clients associate to a wired AP (Access Point)
  Called infrastructure mode; there is also ad-hoc mode with no AP, but that is rare.
Access Point
Client
To Network

## Slide 68: 802.11 Architecture/Protocol Stack (2)
MAC is used across different physical layers

## Slide 69: Basic Service Set & Extended Service Set

## Slide 70: 802.11 physical layer
  NICs are compatible with multiple physical layers
    E.g., 802.11 a/b/g
Name | Technique | Max. Bit Rate
802.11b | Spread spectrum, 2.4 GHz | 11 Mbps
802.11g | OFDM, 2.4 GHz | 54 Mbps
802.11a | OFDM, 5 GHz | 54 Mbps
802.11n | OFDM with MIMO, 2.4/5 GHz | 600 Mbps

## Slide 71: Flow Diagram for CSMA/CA

## Slide 72: 802.11 MAC (1)
  CSMA/CA inserts backoff slots to avoid collisions
  MAC uses ACKs/retransmissions for wireless errors

## Slide 73: 802.11 MAC (2)
Virtual channel sensing with the NAV and optional RTS/CTS (often not used) avoids hidden terminals

## Slide 74: 802.11 MAC (3)
  Different backoff slot times add quality of service
    Short intervals give preferred access, e.g., control, VoIP
  MAC has other mechanisms too, e.g., power save

## Slide 75: 802.11 Frames
  Frames vary depending on their type (Frame control)
  Data frames have 3 addresses to pass via APs

## Slide 76: Subfields in Frame Control field

## Slide 77: Addressing Mechanism

## Slide 78: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching

## Slide 79: Broadband Wireless
  802.16 Architecture / Protocol Stack »
  802.16 Physical Layer »
  802.16 MAC »
  802.16 Frames »

## Slide 80: 802.16 Architecture/Protocol Stack (1)
Wireless clients connect to a wired basestation (like 3G)

## Slide 81: 802.16 Architecture/Protocol Stack (2)
MAC is connection-oriented; IP is connectionless
  Convergence sublayer maps between the two

## Slide 82: 802.16 Physical Layer
Based on OFDM; base station gives mobiles bursts (subcarrier/time frame slots) for uplink and downlink

## Slide 83: 802.16 MAC
Connection-oriented with base station in control
  Clients request the bandwidth they need
Different kinds of service can be requested:
  Constant bit rate, e.g., uncompressed voice
  Real-time variable bit rate, e.g., video, Web
  Non-real-time variable bit rate, e.g., file download
  Best-effort for everything else

## Slide 84: 802.16 Frames
  Frames vary depending on their type
  Connection ID instead of source/dest addresses
(a) A generic frame. (b) A bandwidth request frame
(b)
(a)

## Slide 85: Bluetooth
  Bluetooth Architecture »
  Bluetooth Applications / Protocol »
  Bluetooth Radio / Link Layers »
  Bluetooth Frames »

## Slide 86: Bluetooth Architecture
Piconet master is connected to slave wireless devices
  Slaves may be asleep (parked) to save power
  Two piconets can be bridged into a scatternet

## Slide 87: Bluetooth Applications / Protocol Stack
Profiles give the set of protocols for a given application
  25 profiles, including headset, intercom, streaming audio, remote control, personal area network, …

## Slide 88: Bluetooth Radio / Link Layers
Radio layer
  Uses adaptive frequency hopping in 2.4 GHz band
Link layer
  TDM with timeslots for master and slaves
  Synchronous CO for periodic slots in each direction
  Asynchronous CL for packet-switched data
  Links undergo pairing (user confirms passkey/PIN) to authorize them before use

## Slide 89: Bluetooth Frames
Time is slotted; enhanced data rates send faster but for the same time; addresses are only 3 bits for 8 devices
(b)
(a)
(a)
(b)

## Slide 90: RFID
  Gen 2 Architecture »
  Gen 2 Physical Layer »
  Gen 2 Tag Identification Layer »
  Gen 2 Frames »

## Slide 91: Gen 2 Architecture
Reader signal powers tags; tags reply with backscatter

## Slide 92: Gen 2 Physical Layer
  Reader uses duration of on period to send 0/1
  Tag backscatters reader signal in pulses to send 0/1

## Slide 93: Gen 2 Tag Identification Layer
Reader sends query and sets slot structure
Tags reply (RN16) in a random slot; may collide
Reader asks one tag for its identifier (ACK)
Process continues until no tags are left

## Slide 94: Gen 2 Frames
  Reader frames vary depending on type (Command)
    Query shown below, has parameters and error detection
  Tag responses are simply data
    Reader sets timing and knows the expected format
Query message

## Slide 95: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching

## Slide 96: Data Link Layer Switching
  Uses of Bridges »
  Learning Bridges »
  Spanning Tree »
  Repeaters, hubs, bridges, .., routers, gateways »
  Virtual LANs »

## Slide 97: Uses of Bridges
Common setup is a building with centralized wiring
  Bridges (switches) are placed in or near wiring closets

## Slide 98: Learning Bridges (1)
A bridge operates as a switched LAN (not a hub)
  Computers, bridges, and hubs connect to its ports

## Slide 99: Learning Bridges (2)
Backward learning algorithm picks the output port:
  Associates source address on frame with input port
  Frame with destination address sent to learned port
  Unlearned destinations are sent to all other ports
Needs no configuration
  Forget unused addresses to allow changes
  Bandwidth efficient for two-way traffic

## Slide 100: Learning Bridges (3)
Bridges extend the Link layer:
  Use but don’t remove Ethernet header/addresses
  Do not inspect Network header

## Slide 101: Spanning Tree (1) – Problem
Bridge topologies with loops and only backward learning will cause frames to circulate for ever
  Need spanning tree support to solve problem

## Slide 102: Spanning Tree (2) – Algorithm
  Subset of forwarding ports for data is use to avoid loops
  Selected with the spanning tree distributed algorithm by Perlman
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree which must be sure to span.
So packets can reach every LAN.
First the Root must be selected
By ID it is elected.
Least cost paths from Root are traced
In the tree these paths are placed.
A mesh is made by folks like me
Then bridges find a spanning tree.
– Radia Perlman, 1985.

## Slide 103: Spanning Tree (3) – Example
After the algorithm runs:
    B1 is the root, two dashed links are turned off
    B4 uses link to B2 (lower than B3 also at distance 1)
    B5 uses B3 (distance 1 versus B4 at distance 2)

## Slide 104: Repeaters, Hubs, Bridges, Switches, Routers, & Gateways
Devices are named according to the layer they process
  A bridge or LAN switch operates in the Link layer

## Slide 105: Virtual LANs (1)
VLANs (Virtual LANs) splits one physical LAN into multiple logical LANs to ease management tasks
  Ports are “colored” according to their VLAN

## Slide 106: Virtual LANs (2) – IEEE 802.1Q
Bridges need to be aware of VLANs to support them
  In 802.1Q, frames are tagged with their “color”
  Legacy switches with no tags are supported

## Slide 107: Virtual LANs (3) – IEEE 802.1Q
802.1Q frames carry a color tag (VLAN identifier)
  Length/Type value is 0x8100 for VLAN protocol

## Slide 108: End
Chapter 4